## Slide 1
1.1/ Blue and Green hydrogen are two low-carbon production methods of H2 with the highest future potential
Low-carbon H2
X CO2 emissions
kg CO2 per kgH2 produced
 | Grey H2 | Blue H2 | Green H2
Production process | Split¹ natural gas into H2 and CO2 | Similar to Grey but additionally capture, potentially use, and store CO2 | Split water into H2 and O2 in an electrolyzer that is powered by renewables
CO2 emissions kg CO2/kgH2 | ~10 | ~1-3 Most CO2 stored | ~0 Assuming Green electricity mix²
Investments and complexity | Large scale, one-off facilities Requiring triple-digit million EUR CAPEX per facility | Large scale and one-off facilities Requiring triple-digit mn EUR CAPEX per facility | Small-scale (5-10MW) facilities that can be replicated³ Single/double-digit mn EUR CAPEX per facility, expecting 50-70% reduction until 2030
EPC duration | 3-5 years EPC | 5-10+ years EPC duration, contingent upon development of CO2 storage site | 1-3 years EPC duration
Direct link to power sector | X | X | ✓
1. Process: Sulfur Removal, Synthesis Gas Production via Steam-Methane Reforming (SMR) or Auto-Thermal Reforming (ATR), CO Shift Reaction,
Purification. The latter is expected to offer higher efficiencies in combination with CCS. Grey hydrogen can also be produced from coal gasification.
2. In Australia, producing hydrogen from electrolyzers that run on grid electricity would lead to an emission intensity of ~40 kgCO2/kgH2.
3. Especially PEM electrolyzers can be largely pre-assembled, containerized, and stacked.
McKinsey & Company 4