## Slide 1
1.1/ Blue and Green hydrogen are two low-carbon production
methods of H2 with the highest future potential
X
CO2 emissions
kg CO2 per kgH2 produced
Low-carbon H2
 | Grey H2 | Blue H2 | Green H2
Production process | Split¹ natural gas into H2 and CO2 | Similar to Grey but additionally capture, use, and store CO2 | Split water into H2 and O2 in an electrolyzer powered by renewables
CO2 emissions kg CO2/kgH2 | ~10 | ~1-3 Most CO2 stored | ~0 Assuming Green elec. mix²
Investments and complexity | Large scale, one-off facilities Triple-digit mn EUR CAPEX | Large scale, one-off facilities Triple-digit mn EUR CAPEX | Small-scale (5-10MW), replicable³ Single/double-digit mn EUR CAPEX Expecting 50-70% reduction by 2030
EPC duration | 3-5 years EPC | 5-10+ years EPC, contingent on CO2 storage site development | 1-3 years EPC duration
Direct link to power sector | ✖ | ✖ | ✔
1. Process: Sulfur Removal, Synthesis Gas Production via Steam-Methane Reforming (SMR) or Auto-Thermal Reforming (ATR), CO Shift Reaction,
Purification. The latter is expected to offer higher efficiencies in combination with CCS. Grey hydrogen can also be produced from coal gasification.
2. In Australia, producing hydrogen from electrolyzers on grid electricity would lead to emission intensity of ~40 kgCO2/kgH2.
3. Especially PEM electrolyzers can be largely pre-assembled, containerized, and stacked.
McKinsey & Company 4